## Slide 1
Kinesis
Kinesis · Ankit Prajapati
1
Deep reinforcement learning for
simulated mobile-robot path tracking
Pure Pursuit and SAC under shared constraints
Both finish the nominal routes.
The conventional baseline tracks more accurately.
28 October 2026
Notes: Introduce this as a simulation portfolio project. The question was whether learned continuous-action control adds value beyond a conventional tracker. The simulator, integration and evaluation are implemented here; SAC comes from Stable-Baselines3. No physical robot or deployment is claimed. Repository: https://github.com/sp-ankitprajapati/kinesis

## Slide 2
Robot model and control task
Kinesis · Ankit Prajapati
2
dx/dt = v cos θ
dy/dt = v sin θ
dθ/dt = ω
Speed response includes actuator lag.
Control updates occur every 0.1 s.
Setting | Value
Forward speed | 0–1.2 m/s
Turn rate | −2 to 2 rad/s
Response constants | 0.25 s / 0.18 s
Integration | 5 substeps
Planar kinematic abstraction; no hardware validation
Notes: The state contains x, y, heading, linear speed and turn rate. Unicycle kinematics and first-order response provide a small differential-drive-style abstraction. Five substeps approximate changing twist. Analytic motion checks and convergence tests validate important boundaries. Wheel mechanics, slip, obstacles, collisions, sensing pipelines and physical safety are omitted. Evidence: kinesis/dynamics.py; tests/test_dynamics.py.

## Slide 3
Shared observations and completion rules
Kinesis · Ankit Prajapati
3
25 observation values
Reference points in the robot frame
Tracking error, heading and current speeds
Previous action and command-delay queue
Next route gate and remaining time
Success requires every ordered gate and the endpoint.
Stopping or skipping the route does not count.
Notes: Both controllers consume the same 25-value public observation, with no privileged state access by Pure Pursuit. Sine/cosine avoids angle discontinuities. A two-slot pending-action queue and delay length represent command delays. Gates every 0.5 m must be reached in order within 0.35 m. Success also requires endpoint proximity and near-complete progress. Stopping is penalized; missed gates fail. Some cutting within tolerance remains possible and is reflected in error metrics. Evidence: kinesis/env.py; docs/learning-report.md.

## Slide 4
Validation before held-out testing
Kinesis · Ankit Prajapati
4
Split | Scenarios | Purpose
Training | 24 | Policy experience
Validation | 12 | Choose controller settings
Test | 24 | Final paired comparison
4 candidate settings per method
SAC: 3 independent seeds × 80,000 final training steps
Equal candidate counts; different computational tuning costs
Notes: Route hashes check exact split separation. Training and validation use straight, sine and arc families. Test cases change parameters and initial conditions and include six unseen double-sine paths. Each method has four candidate settings on the same validation scenarios, with unequal computational tuning costs. SAC pilots use 12,000 steps with seed 101. The selected configuration is retrained under seeds 7, 17 and 27 for 80,000 steps each. All final checkpoints are tested. The representative plot seed is chosen on validation before testing. Evidence: artifacts/protocol.json, frozen_controllers.json and manifests/.

## Slide 5
Training returns vary across random seeds
Kinesis · Ankit Prajapati
5
Chart: 
Environment steps → | Episode return: 20-episode moving mean
Notes: These are training episodes only, using a 20-episode moving average. Reward is not a substitute for tracking error or robustness. Every seed is retained. Final learning calls total 11.13 minutes on two vCPUs, excluding pilots, evaluation, setup and reporting. One PyTorch thread and two 64-unit hidden layers were used. No GPU was used. Evidence: artifacts/training/seed_*/monitor.csv and run.json. SAC source: https://stable-baselines3.readthedocs.io/en/master/modules/sac.html

## Slide 6
Pure Pursuit tracks more accurately
Kinesis · Ankit Prajapati
6
Nominal metric | Pure Pursuit | SAC mean ± seed SD
Success, 24 routes | 100% | 100% ± 0%
Tracking RMSE (m) | 0.043 | 0.113 ± 0.066
Elapsed time (s) | 12.65 | 12.24 ± 1.02
Angular slew RMS (rad/s²) | 0.59 | 5.91 ± 2.18
Mean median inference (ms) | 0.032 | 0.390 ± 0.058
SAC: mean ± sample SD across 3 seeds; no significance claim
Notes: All four controllers completed all 24 nominal routes, including six double-sine paths. SAC figures are mean plus/minus sample standard deviation over three seeds, not confidence intervals. The baseline has lower error, angular command slew and prediction time. Some SAC seeds finish faster, but no overall advantage is established. Latency is CPU wall time around prediction, excluding simulator work; it is not embedded worst-case timing. Evidence: artifacts/test_results.json and docs/results.md.

## Slide 7
An unseen double-sine test route
Kinesis · Ankit Prajapati
7
Chart: 
x and y in metres · fixed scenario 003 · SAC seed 27 chosen on validation
Notes: This is fixed test scenario 003, not the best test example. Seed 27 was selected for plots on validation before testing. All seeds remain in the report. Both controllers have the same finite reference previews. This editable plot uses recorded positions and known reference geometry. Six cases of this family do not establish arbitrary-path generalization. Evidence: artifacts/traces/ and models/manifest.json.

## Slide 8
Command delay exposed SAC failures
Kinesis · Ankit Prajapati
8
Chart: 
| Nominal | Noise | 200 ms delay | Slower response
Pure Pursuit | 100 | 100 | 100 | 100
SAC, mean of 3 seeds | 100 | 100 | 90.2778 | 100
Success (%) · SAC delay: 65 / 72 attempts · PP delay: 24 / 24
Notes: Disturbances are tested separately: Gaussian 0.03 m position noise per coordinate and 3 degree heading noise; two-step or 200 ms delay; or 2.5 times response time constants. Pure Pursuit completed 96/96 attempts across conditions. SAC delay completion was 65/72: seed 7 had no failures, seed 17 missed four gates, and seed 27 missed two gates and reached one time limit. Queue state is observed, but nominal training never exposes nonzero delay, so this also changes the queue-input distribution. Combined disturbances were not tested. Evidence: artifacts/test_episodes.csv.

## Slide 9
Engineering conclusions and next work
Kinesis · Ankit Prajapati
9
Keep the conventional baseline
SAC learned route completion, but did not improve the full metric set.
Delay tests exposed failures hidden by nominal success.
Next: disturbance training, broader scenarios and more seeds.
Physical deployment needs separate modelling and validation.
Implemented: simulator, integration and evaluation
Library algorithm: Stable-Baselines3 SAC
Notes: For this simulator and budget, Pure Pursuit is the stronger default. SAC learns nominal completion but does not improve the full metric set; delay exposes failures. Implemented contributions are the simulator, controller integration, safeguards, experiments and evaluation. SAC comes from Stable-Baselines3/PyTorch. Extensions could add training-time disturbances, broader scenarios, more seeds and identified dynamics, then optional ROS2. They are future work. No physical robot, motorcycle dynamics, embedded deployment or safety validation is claimed. Sources: docs/results.md; docs/learning-report.md; https://publications.ri.cmu.edu/implementation-of-the-pure-pursuit-path-tracking-algorithm